## Slide 1: ESOP Synthesis
R09921049
黃禹靖

## Slide 2: ESOP Synthesis
Exclusive Sum of Product
ESOP are advantageous for quantum circuits because of their natural relation to Toffoli gates.
Toffoli gate is one of the primitives in reversible logic.

## Slide 3: ESOP Synthesis
By concatenating Toffoli gates on the same target line, we can build up an ESOP expression.

## Slide 4: ESOP Synthesis
The Toffoli gates are mapped into quantum gate library (Clifford+T gate set).
A heuristic to reduce the cost of mapped quantum circuits: minimize
  Number of Toffoli gates → Number of cubes
  Number of control lines → Number of literals

## Slide 5: ESOP Synthesis
It is necessary to convert a Boolean network into minimum two-level ESOP expressions.
Two state-of-the-art techniques
  AIG extract
  BDD extract

## Slide 6: AIG BDD Extract
AIG method suffers from size explosion of resulting ESOP expressions.
BDD method suffers from memory explosion in BDD construction process.

## Slide 7: Divide and Conquer Method
Lemma Any Boolean function f can be written as if
Selection of a set P Limit our choices to is single-cube cofactor.

## Slide 8: Selection Heuristic
Fixed variable selection
Free variable selection
Support threshold

## Slide 9: BDD Extract
Pseudo-Kronecker Expressions
A Boolean function can be represented by any of the three formulae:
  Shannon expansion
  Positive Davio expansion
  Negative Davio expansion
Either of three expansion can be applied recursively until constant function reached.

## Slide 10: BDD Extract
Shannon
Negative Davio
Multiply out

## Slide 11: BDD Extract
Find the expansion that minimize total cube number

## Slide 12: ESOP simplify
Proposition
  Two identical cubes can be added or removed
  The XOR of two distance-1 cubes can be represented by a single cube.
Example

## Slide 13: Experimental Results
16-adder |  |  |  | simplified |  | 
PO | Support # | Cube # | Literal # | Cube # | Literal # | time (s)
cout | 33 | 244607 | 7506370 | 244607 | 7506370 | 4630.2
s15 | 33 | 82332 | 2438338 | 82268 | 2437378 | 694.42
s14 | 31 | 41164 | 1136834 | 41132 | 1136418 | 211.99
s13 | 29 | 20580 | 527250 | 20564 | 527074 | 70.62
s12 | 27 | 10288 | 243042 | 10280 | 242970 | 28.63
s11 | 25 | 5142 | 111230 | 5138 | 111202 | 17.08
s10 | 23 | 2569 | 50470 | 2567 | 50460 | 5.28
c432 |  |  |  | simplified |  | 
PO | Support # | Cube # | Literal # | Cube # | Literal # | time (s)
G223gat | 18 | 512 | 4609 | 511 | 4608 | 0.12
G329gat | 27 | 5448 | 79378 | 3952 | 60855 | 7.05
G370gat | 36 | 110176 | 2267008 | 85739 | 1811954 | 773.83
G421gat | 36 | 31414 | 685194 | 25831 | 578819 | 127.39
G430gat | 36 | 91969 | 1910788 | 69089 | 1468765 | 544.47
G431gat | 36 | 84303 | 1748731 | 65682 | 1382563 | 470.6
G432gat | 36 | 76912 | 1565663 | 59103 | 1235378 | 400.34

## Slide 14: Experimental Results
Support Threshold = 20 |  |  |  |  |  | 
c432 |  |  |  | simplified |  | 
PO | Support # | Cube # | Literal # | Cube # | Literal # | time (s)
G223gat | 18 | 512 | 4609 | 511 | 4608 | 0.12
G329gat | 27 | 5448 | 79378 | 3952 | 60855 | 7.05
G370gat | 36 | 110176 | 2267008 | 85739 | 1811954 | 773.83
G421gat | 36 | 31414 | 685194 | 25831 | 578819 | 127.39
G430gat | 36 | 91969 | 1910788 | 69089 | 1468765 | 544.47
G431gat | 36 | 84303 | 1748731 | 65682 | 1382563 | 470.6
G432gat | 36 | 76912 | 1565663 | 59103 | 1235378 | 400.34
Support Threshold = Inifinity |  |  |  |  |  | 
c432 |  |  |  | simplified |  | 
PO | Support # | Cube # | Literal # | Cube # | Literal # | time (s)
G223gat | 18 | 512 | 4609 | 511 | 4608 | 0.12
G329gat | 27 | 2816 | 39203 | 2055 | 29955 | 124.49
G370gat | 36 | - | - | - | - | -
G421gat | 36 | - | - | - | - | -
G430gat | 36 | - | - | - | - | -
G431gat | 36 | - | - | - | - | -
G432gat | 36 | - | - | - | - | -

## Slide 15: Thank you!